## Slide 1
An Update on the UK Smart X-Ray Optics Project
Alan Michette & Sławka Pfauntsch
King’s College London Department of Physics
With acknowledgements to the UK Smart X-Ray Optics Consortium
University College London
The University of Leicester
The Scottish Microelectronics Centre, University of Edinburgh
The University of Birmingham
The Mullard Space Science Laboratory
STFC Daresbury Laboratory
Diamond Light Source Ltd Silson Ltd
funded by the EPSRC under the Basic Technology Programme Grant Code D04880X,
and to
Tongji University, Shanghai
funded by Innovation China UK & the Royal Society.
And, of course, supported by EU COST Action MP0601
Short Wavelength Laboratory Sources

## Slide 2
Outline
Review of “Conventional” X-Ray Optics
Refractive, Reflective, Diffractive
and their limitations.
Smart X-Ray Optics
Microstructured Optical Arrays
Applications of Focused X-Ray Probes formed from Microfocus X- Ray Sources
Summary and Conclusions

## Slide 3
Summary of “Conventional” X-Ray Optics
Note – combinations of optics, e.g., reflective-diffractive as in Bragg-Fresnel lenses, have also been used. These tend to also combine the advantages and disadvantages.
 | Suitable for Energy Angle |  | Advantages | Disadvantages
CRLs | >5keV | Normal | “Simple” Insensitive to misalignment | Chromatic aberration Limited resolution
Grazing | Any | <θC | Achromatic Widely used | Need compound systems Aberrations
Periodic MLMs | Soft | Any | Good wavelength / angle selectivity Wide range of possibilities | Narrowband Susceptible to damage
Aperiodic MLMs | Soft | Any | Broadband Wide range of possibilities Less sensitive to manufacturing errors | Harder to make Less selective
ZPs | “Any” | Normal1 | Good spatial resolution Multiplicity of foci | Inefficient Small apertures
1Can also be used in reflection at grazing incidence

## Slide 4
We want to study a range of problems in radiation biology:
How are biological cells damaged by ionising radiation?
More specifically, how is response to radiation distributed
across a cell? What is a “safe” dose?
How significant is damage to components other than nuclear DNA?
Prior to the development of a focused x-ray microprobe some results, using α particles, suggested that cytoplasm damage (presumably mitochondrial DNA) may be important.
Can damage effects be transmitted to un-irradiated cells — the neighbourhood effect?
Statistical analyses of experiments with unfocused x-ray beams had previously suggested that they may be.
Are temporal effects important?
The King’s College X-Ray Microprobe

## Slide 5
Historically, experiments using x-rays to study radiation damage were carried out using unfocused beams.
The low-dose responses of cells were  hard to determine as, with soft x-rays, the dose imparted by just a few photons is damaging (1Gy=1J/kg  ~10 absorbed carbon K photons in a cell nucleus). But if the beam is unfocused, the precise dose to each cell is unknown.
How is response to radiation distributed across a cell?
Some results have been obtained using α particle and proton probes, but it is not easy to control the precise location of dose within a cell.
Questions like these cannot be answered using unfocused beams: at low dose it cannot be known which cells or parts of cells were irradiated; at high dose it is likely that most cells and several parts of the cell were.
How significant is damage to components other than nuclear DNA?
Can damage effects be transmitted to un-irradiated cells — the neighbourhood effect?
The King’s College X-Ray Microprobe

## Slide 6
The King’s College X-Ray Microprobe
High-dose extrapolation
Low-dose data
Microprobing of biological cells using sub-micrometre spots of focused carbon K x-rays (284eV) has been very successful in studies relevant to radiation-induced cancers, including:
Low-dose effects, including low-dose hypersensitivity (what is a safe dose?).
The bystander effect; if only one cell out of a population in a dish is irradiated, up to ~10% do not survive.
Comparison of cytoplasm and nucleus irradiation; around the same percentage of cells seem to survive irrespective of whether the nucleus or cytoplasm is specifically irradiated. This suggests that damage to both nuclear and mitochondrial DNA is important.

## Slide 7
Thus tissue samples, of much more importance for radiation effects in living organisms, cannot be studied.
C K x-rays can only penetrate one cell; essentially zero pass through unabsorbed.
There will always be some cytoplasm irradiation even when the nucleus is targeted.
To study tissue samples higher energies are needed; chromium Ka (5.4keV) x-rays are suitable.
So far it has only been possible to study effects related to cell death, rather than mutations which are much more important in cancer studies. Fortunately, mutations are much rarer; on average, if ≈10,000 cells are given a specific (low) dose, ≈9999 will repair correctly or die; only ≈1 will repair incorrectly (mutate). Very few of those that do mutate are potentially cancerous.
 But there are problems ...
The King’s College X-Ray Microprobe

## Slide 8
Monochromator
Experiments so far have been done using zone plates, with a focal spot size limited by the demagnified source.
Source exit window
Zone plate
Pinhole (OSA)
Cells on xyz stage
UV assay microscope
Source size ≈5µm, focal spot ≈0.2µm for C K,
≈4µm for Cr K, since f E.
Focused flux limited by:
(mononchromatic) source output; efficiency and aperture of optic (Aeff~10-9 for a typical zone plate).
To study mutations in tissue samples, and to disentangle nucleus/cytoplasm effects, need:
smaller source size (≈1µm);
higher demagnification;
higher efficiency and/or aperture optic —
all at keV energies
higher source output;
These factors define the design goals of the new microprobe.
, with 24/7 access.
The King’s College X-Ray Microprobe

## Slide 9
Now planning to use liquid N2 cooled chromium, melting point 2180K and thermal conductivity 94W/m/K.
The Microfocus Source
How can we get a 1µm source size?
This limits the beam current, in order to limit divergence which would increase the size of the electron focus.
FEA calculations show that ~1mA can be focused into a ~1µm spot, a power density of ~2x1013W/m2.
The original plan was to use a titanium target (4.5keV), but at such power densities Ti will melt (FEA), even with liquid N2 cooling, due to its low melting point (1935K) and thermal conductivity (22W/m/K).
The electron accelerating voltage must not be too high, to optimise K x-ray production, limit secondary electron range and prevent high energy bremsstrahlung — 15keV selected as suitable for ~5keV x-rays.

## Slide 10
Grazing incidence reflective arrays loosely based on polycapillaries.
Piezo coated (unimorph or bimorph).
Arrays can be bent either actively or adaptively to reduce aberrations and/or to provide variable focus and magnification.
The aim is to provide significantly more focused flux in a sub- micrometre spot than can be achieved with a zone plate.
Current status: Modelling using ray tracing and finite element analysis. Prototype components developed, tested & improved.
Single or multiple purpose-built arrays.
Polycapillary optics use bundles of capillaries, e.g., microchannel plates, to provide multiple grazing incidence reflections along many circular, or square, or hexagonal ... channels. Useful as relay optics, but limited resolution capabilities.
Micro-Structured Optical Arrays

## Slide 11
Micro-Structured Optical Arrays
Quasi-circularly symmetric or straight arrays of channels etched into silicon (and possibly coated).
By using single grazing incidence reflections in each of two arrays the Abbe sine can be approximately satisfied, thereby reducing aberrations.
Bending one or both arrays can further reduce aberrations and give variable focal length.
Prototype design for 5.4keV:
With ≈1nm sidewall roughness, as achieved by wet etching, this gives over 100× as much focused flux as a typical zone plate — even more if the application allows bremsstrahlung to be used.
focal length ≈5cm.
≈10µm channels, 20µm period
2mm diameter (2mm square for 1D prototype)
50-200µm thick silicon
second component bending radius ≈5cm

## Slide 12
Micro-Structured Optical Arrays
First attempts at bending by direct piezo actuation were also not successful; minimum radius of curvature was ≈15cm (FEA and experiment).
Mechanical bending induced high stress points and was bulky.
Now trying indirect piezo actuation, using an arrangement of levers — the “spider array”; FEA suggests this will work.*
*The originator of the “spider array” concept is Daniel Rodriguez-Sanmartin, University of Birmingham
An average bending radius of 5cm can be achieved, with an approximately parabolic profile (giving a better focus than a circular one) at a maximum stress of ≈40% of the silicon breaking stress.
Now exploring ways of making these, through a combination of (directional) wet etching for the active channels (to get the smooth walls) and dry etching for the levers (to get the angles needed).‡
‡The arrays are made by Camelia Dunare, Scottish Microelectronics Centre

## Slide 13
Micro-Structured Optical Arrays
A preliminary analysis suggests that the peak reflectivity is a few percent (at a much larger glancing angle than will be used in practice), consistent with the AFM measured channel wall roughness of 1.2nm.
Reflectivity Tests
*The measurements were done by Charlotte Feldman, University of Leicester.
The reflectivity of an unbent wet etched array was measured using ≈500eV x-rays, by relatively rotating the source and array in front of a CCD.*
0° is defined as the angle at which most x-rays should be reflected. Away from 0° the observed count rate falls since more x-rays pass straight through (negative angles) or undergo multiple reflections (positive).
Reflectivity was expected over a range of ≈5°. The fitted Gaussian peak is at 0.2°, with a FWHM of 5.3°.

## Slide 14
Summary
 Soft x-ray microprobes have demonstrated their use in studying a range of problems in radiation biology of single cells.
 But to extend these studies to mutation effects in tissue samples, it is necessary to:
 Use higher energy x-rays;
 Deliver more focused flux.
 It seems feasible that these goals can be achieved by:
 Using a chromium microfocus source with a ≈1µm source size (under construction);
 Using microstuctured optical array optics, with Aeff>100x that of a typical zone plate.
 May need to define a route to true 2-D focusing.